## Slide 1: Communication Theory CIE 337
Marwan Ahmed 202101214
Amr Ashraf 202101355
Amr Ahmed 202100302

## Slide 2: PART A: PAM MODULATION
To modulate the message signal, we first need to make the Train of pulses with the specified Ts (pulse period) and T (pulse on time)

## Slide 3
Then: we get our message signal

## Slide 4
Then: we multiply the pulse signal with the message signal to obtain the modulated signal

## Slide 6: Demodulation
To demodulate the received signal, we pass it to a (lop pass filter) with cutoff frequency more than message bandwidth (B) and less than (Fs – B) and then apply a suitable gain

## Slide 7: Test cases:
Message 1: with (Ts = 1/8) and (T = 0.25 * Ts) and (t = 0: 0.001: 1)

## Slide 8: Test cases:
Message 2: with (Ts = 0.4) and (T = 0.1) and (t = 0: 0.01: 8)

## Slide 9: PART B: FLAT-TOP PAM MODULATION:
To modulate the message signal, we get our message signal

## Slide 10
Then: we sample it

## Slide 11
Then: we enter the sampled signal to a pulse generator which output is rectangle at each pulse

## Slide 13: Demodulation
To demodulate the received signal, we pass it to a (lop pass filter) with cutoff frequency more than message bandwidth (B) and less than (Fs – B) and then apply a suitable gain

## Slide 14: Test cases:
Message 1: with (Ts = 1/8) and (T = 0.25 * Ts) and (t = 0: 0.001: 1)

## Slide 15: Test cases:
Message 2: with (Ts = 0.4) and (T = 0.4) and (t = 0: 0.01: 8)

## Slide 16: PART C: PWM MODULATION
We first get our message signal

## Slide 17
Then: we make a train of triangle pulses

## Slide 18
Then: we enter the two signals to a comparator which gives True only when the message signal amplitude is higher the pulse signal amplitude

## Slide 19
Which gives the modulated signal as the output

## Slide 20: Demodulation:
To demodulate the received signal, we need to convert it to a PAM signal then we pass it to a (lop pass filter) with cutoff frequency more than message bandwidth (B) and less than (Fs – B) and then apply a suitable gain, we can do this by enter the signal to a integrate and sample device which give us the PAM version of our signal:

## Slide 21
Then: we enter it to a low pass filter to generate the original signal

## Slide 22: Test cases:
Message 1: with (Ts = 1/8) and (A = 2) and (t = 0: 0.001: 1)

## Slide 23: Test cases:
Message 2: with (Ts = 0.4) and (A = 2) and (t = 0: 0.01: 8)

## Slide 24: PART D: PPM MODULATION
We do the same steps as PWM but after that we enter the signal to a pulse generator which only generate fixed width pulses at the end of the widths of the PWM

## Slide 26: Demodulation:
We convert the signal back to the PWM signal using SR flip-flop (we enter Pulse generator signal to the R input, and enter a reference pulse signal to the S input), due to the set and reset signals applied to the flip-flop, we get a PWM signal at its output. The PWM signal can be demodulated using the PWM demodulator as explained above in the report.

## Slide 27: Test cases:
Message 1: with (Ts = 1/8) and (T = 0.1*Ts) and (A = 2) and (t = 0: 0.001: 1)

## Slide 28: Test cases:
Message 2: with (Ts = 0.4) and (T = 0.05) and (A = 2) and (t = 0: 0.01: 8)

## Slide 29
Thank you